## Slide 1: Ghost Tunnel Data transmission based on WiFi covert channel
Chengqiang Jin,M.S.
College of Computer Science and Technology
Zhejiang University of Technology
king_jcq@163.com

## Slide 2
Agenda
Introduction
Previous research on Ghost Tunnel
Ghost Tunnel implementation
Further application of Ghost Tunnel

## Slide 3
Introduction
Air-Gapping
Attack payload

## Slide 4
Air gapping
Air gapping
- Wikipedia: “air gapping is a network security measure employed on one or more computers to ensure that a secure computer network is physically isolated from unsecured networks, such as the public Internet or an unsecured local area network. The name arises from the technique of creating a network that is physically separated (with a conceptual air gap) from all other networks.”
Air gapping aims to avoid the intrusion and data leakage
through network connections

## Slide 5
Stuxnet Worm(2010)
Attacking initiated viaan infected USB drive
Designed to attack the Yilan nuclear

## Slide 6
Attack Payload - 1
Transmission of data using infrasonic waves or ultrasonic

## Slide 7
Attack payload – 2
Stealing computer data from a power line

## Slide 8
Attack payload – 3
HID attack

## Slide 9
Previous research on Ghost Tunnel

## Slide 10
PegasusTeam, 360 Security Technology

## Slide 11
Comman WiFi Connection

## Slide 12
A covert WiFi channel using Beacon, Probe Request, Probe Response
A special SSID as the identifier
Ghost Tunnel – No WiFi Connection

## Slide 13
Ghost Tunnel implementation

## Slide 14
Beacon/Probe Response
Beacon帧结构

## Slide 15
Probe Request
Probe request帧结构

## Slide 16
Windows
  - Native Wifi API
Mac OSX
  - coreWLAN
Linux
  - nl80211 & libnl
Through Operating System WiFi API

## Slide 17
uSSIDLength | ucSSID(payload)
dwDataSize | ElementID | Length | Information(payload)
DWORD WINAPI WlanScan(
  _In_ HANDLE hClientHandle,
  _In_ const GUID *pInterfaceGuid,
  _In_opt_ const PDOT11_SSID pDot11Ssid,
  _In_opt_ const PWLAN_RAW_DATA pIeData,
  _Reserved_ PVOID pReserved );
DOT11_SSID pDot11Ssid
WLAN_RAW_DATA pIeData
Windows Platform

## Slide 18
Vendor element
ElementID(dd) | Payload Length | Payload
Hostapd

## Slide 19
插入捕获数据图片

## Slide 20
Further application of Ghost Tunnel

## Slide 21
transfer files

## Slide 22
ElementID(dd) | Payload Length | Total Fragment | Fragment ID | Payload
ElementID(dd) | Payload Length | Payload
fragmentation
理论长度计算